INFECTION CONTROL RISK ASSESSMENT AND PERMIT

| Project Name: | Project Location: |
| --- | --- |
| FDC# | Project Manager: Contact # |
| Contractor: | Superintendent: Contact #: |
|  | CONSTRUCTION ACTIVITY |  | INFECTION CONTROL RISK GROUP |
|  | TYPE A: Inspection, non-invasive activity |  | GROUP 1: Low Risk |
|  | TYPE B: Small scale, short duration, moderate to high levels |  | GROUP 2: Medium Risk |
|  | TYPE C: Generates moderate to high levels of dust, requires more than 1 work shift for completion. |  | GROUP 3: High Risk |
|  | TYPE D: Major demolition and construction activities requiring consecutive work shifts. |  | GROUP 4: Highest Risk |
| CLASS I Date: Initials: | 1. Execute work by methods to minimize raising dust from construction operations. 2. Immediately replace any ceiling tile displaced for visual inspection. 3. Clean up and disposal in accordance with defined procedures. |  |
| CLASS II Date: Initials: | 1. Obtain infection control permit prior to construction. 2. Provide active means to prevent air-born dust from dispersing into atmosphere. 3. Water mist work surfaces to control dust while cutting. 4. Seal unused doors with tape. 5. Block off and seal air vents. 6. Wipe surfaces with approved disinfectant. | 7. Contain construction waste before transport in tightly covered containers. 8. Wet mop and/or vacuum with HEPA filtered vacuum before leaving work area. 9. Place dust mat at entrance and exit of work area. |
| CLASS III Date: Initials: | 1. Obtain infection control permit prior to construction. 2. Isolate HVAC system in area where work is being done to prevent contamination of the duct system. 3. Complete all critical barriers or implement control cube method before construction begins. 4. Maintain negative air pressure within work site utilizing HEPA equipped air filtration units. 5. Seal holes, pipes, conduits and punctures appropriately. 6. Place dust mat at entrance and exit of work area. 7. Vacuum work area with HEPA filtered vacuum. 8. Wet mop with approved disinfectant. | 9. Materials transported into or out of the site must be tightly covered or wrapped in plastic. 10. Construction waste must be transported in tightly covered containers. Wipe down carts, covers and wheels with disinfectant before leaving area. 11. Wipe down all surfaces, HEPA vacuum and mop area with approved disinfectant prior to removing barriers. 12. Do not remove barriers from work area until completed project has been thoroughly cleaned. 13. Upon completion, restore HVAC system in areas where work has been performed. |
| CLASS IV Date: Initials: | 1. Obtain infection control permit prior to construction. 2. Isolate HVAC system in area where work is being done to prevent contamination of the duct system. 3. Complete all critical barriers or implement control cube method before construction begins. 4. Maintain negative air pressure within work site utilizing HEPA equipped air filtration units. 5. Seal holes, pipes, conduits and punctures appropriately. 6. Construct anteroom and require all personnel to pass through this room so they can be vacuumed using a HEPA vacuum cleaner before leaving work site OR they can wear cloth or paper coveralls that are removed each time they leave the work site. 7. Place dust mat at entrance and exit of work area. | 8. Vacuum work area with HEPA filtered vacuum. 9. Wet mop with approved disinfectant. 10. Materials transported into or out of the site must be tightly covered or wrapped in plastic. 11. Construction waste must be transported in tightly covered containers. Wipe down carts, covers and wheels with disinfectant before leaving area. 12. Wipe down all surfaces, HEPA vacuum and mop area with approved disinfectant prior to removing barriers. 13. Do not remove barriers from work area until completed project has been thoroughly cleaned. 14. Upon completion, restore HVAC system in areas where work has been performed. |
| Additional ICRA Requirements: |
| Requested by: Date: | ICRA Authorized by: Date: |
| Contractor: Date: |  |

TJC Standard EC 02.06.05 states that space must be managed during demolition, renovation or new construction to reduce risk to those in the organization. This form addresses Elements of Performance 2 and 3.

Form Date 07/10/2015